## Slide 1
P4 Programmable Traffic Management
Stephen Ibanez & Gordon Brebner
9/12/2018
Notes: Hello my name is Stephen Ibanez and I’m a PhD student at Stanford University working with Nick McKeown. And I’ve spent the summer as an intern in Xilinx Labs working with Gordon Brebner.
I’ve very excited to be here today to talk to you guys about our work in exposing programmability of traffic management functions to P4 programs.

## Slide 2: Goals
Motivating Discussions
Traffic Manager Architectural Model Overview
Putative P4 Extensions
Moving Forward Discussions
Notes: Here’s a list of the main goals that we have for today.
I’ll start off will some motivating discussions and explain why we should care about traffic management today and then try to convince you why we should make traffic management functionality programmable.
I’ll provide an overview of the architectural model that we are proposing to use for building programmable traffic managers. This architectural model is about at the same level of abstraction as the PISA model, so that’s the mindset that you should have when we go through that.
In order to program this architectural model, we’ve put together some potential P4 language extensions. So I’ll walk through some example programs so you can see how we can write TM programs in P4.
Although, I want to say upfront that we haven’t run these language extensions by the language working group so they are not in any way set in stone. The may in fact be more convenient abstractions that can be used to program our model. The reason for talking to you guys (the architecture WG) first is so that we can settle on the underlying architectural model before deciding upon the exact language semantics that should be used to program it.
I also hope to leave plenty of time at the end for discussions so we can decide how best to move forward with this proposal.

## Slide 3: What is Traffic Management?
Packet Scheduling – in what order?
Traffic Shaping – at what rate/pacing?
Policing – is packet compliant?
Drop Policy – how to avoid / deal with congestion?
Packet Buffering – how to store packets?
Packet Replication – how to replicate packets?
Classification – how to map packets into queues?
Notes: First and foremost, what is traffic management? The term gets thrown around a lot and it is a broad topic that covers many different functions.
For the purposes of this talk, we will divide the traffic management function space into the following categories:
Packet scheduling – this is the algorithms that decides the order in which to send out packets. There are many existing scheduling algorithms, probably the common is fisrt-in-first-out or FIFO, but there is also LIFO, WFQ, priority queueing, etc
Traffic Shaping – this algorithm decides when to send out packets, that is the rate & pacing. Token bucket rate limiting is a common shaping technique
Policing decides whether or not each packet is in compliance with some predefined service agreement. If it’s not then it takes some corrective action such as dropping the packet, decrementing it’s priority, marking a header fields, etc
The drop policy decides how to avoid or deal with congestion. Tail drop is probably the most common drop policy, which simply drops an incoming packet if there is not enough room for it in the queue. But there is others as well such as RED/WRED
Packet buffering decides how to actually store packets in memory
Packet replication decides how to replicate packets to one of more output ports
Classification is another function that is closely related to TM and it decides how to map packets into queues
We will discuss how to make the red ones programmable today

## Slide 4: Where are traffic managers used?
Integrated Switch (PISA)
NIC or Line Card
Ingress M/A
Ingress Parser
Egress Deparser
Egress M/A
Ingress Deparser
Traffic Manager
Egress Parser
Ingress M/A
Ingress Parser
Egress Deparser
Egress M/A
Ingress Deparser
Egress Parser
Host PCI Express (NIC) /
Switch Fabric (Line Card)
Ethernet Ports
Traffic Manager
Traffic Manager
Notes: Traffic managers appear in a variety of contexts, within each context they may have different requirements and objectives

## Slide 5: Why should we care about Traffic Management?
Lots of different types of traffic w/ different characteristics and requirements:
  Characteristics: burstiness, packet sizes, flow sizes, flow rates
  Requirements: throughput, latency, loss, jitter, reordering, flow completion time, tail latency
Network operators have a wide range of objectives:
  Meet all SLAs
  Maximize network utilization
  Achieve fairness
Network devices are picking up more functionality
About 50% of a modern programmable switch chip is dedicated to buffering and traffic management logic – but is not programmable!
More network programmability
More types of traffic
More TM requirements!
More complicated ASICs
Embrace programmability!
Notes: Now I’ll try to convince you why we should care about traffic management.
Today’s networks have lots of types of traffic with different characteristics and different performance requirements…
At the same time, network operators have a number of objectives they would like to achieve…
We use these characteristics, requirements, and objectives to formulate requirements for our traffic managers.
Now that P4 is starting to become adopted we are seeing network devices pick up new functionality and new types of traffic are emerging with new requirements.
For instance NetChain is a paper from NSDI 2018, which describes a system that provides an ultra low latency KV store entirely in the data-plane of a network. In order to provide strong consistency and fault tolerance it uses direct switch to switch communication without any latency added by end host software stacks. This means that every nanosecond matters a lot. If a packet gets delayed by 100ns that could already be 10% overhead. So it doesn’t really make sense to treat this the same as traffic that we currently treat as low latency, which can typically tolerate delays of at least a couple microseconds. So how are we going to deal with these new requirements on the TM?
Small menu of sched algs to choose from

## Slide 6: Why should we care about Traffic Management?
WAN links are expensive  want to make best use of them by prioritizing traffic
Modern congestion control algorithms rely on accurate packet pacing (e.g. BBR[1], Timely[2])
Performance isolation for thousands of VMs (millions of flows) per server
[1] Cardwell, Neal, et al. "BBR: Congestion-based congestion control." Queue 14.5 (2016): 50.
[2] Mittal, Radhika, et al. "TIMELY: RTT-based Congestion Control for the Datacenter." ACM SIGCOMM Computer Communication Review. Vol. 45. No. 4. ACM, 2015.
[3] Saeed, Ahmed, et al. "Carousel: Scalable traffic shaping at end hosts." Proceedings of the Conference of the ACM Special Interest Group on Data Communication. ACM, 2017.
Notes: Traffic management is very important in the WAN context where links are very expensive, so we want to make sure that we are properly prioritizing the important traffic over the less important traffic.
Modern congestion control algorithms – use fine grained packet pacing to avoid packet drops for video traffic and incast traffic patters.
Modern cloud providers need to reliably isolate performance for millions of flows within the data center to ensure predictable performance, otherwise cloud services can become unavailable – this is accomplished using traffic management
I hope you’re convinced that traffic management is indeed an important topic today.

## Slide 7: Benefits of Programmable Traffic Management
Benefits of an unambiguous way to define TM algorithms:
  Portability
  Formal verification and static analysis
  Precise way to express customer needs
Benefits of having programmable TM:
  Innovation
  Differentiation
  Reliability
  Network operators can fine tune for performance
  Small menu of algorithms to choose from today
  Many possible algorithms that can be expressed
Notes: Now I’ll spend some time explaining why we think traffic management functions should become programmable.
Aside form the benefits of actually having programmable hardware, there are a number of benefits from just defining an unambiguous way to express TM algs.
There is no standard way of talking about TM algorithms today. Vendors describe the TM capabilities of their devices in English and the customer must interpret this. So defining a standard language would certainly be a first step towards achieving consistent and predictable performance of TM algorithms across devices from different vendors, and eventually portability of TM programs.
portability and predictable performance of TM algorithms across devices from different vendors.
No standard way to describe TM algorithms today
Reliability – remove unused features

## Slide 8: Existing TM algorithms are too limiting
TM algorithm parameters can be derived from:
  Network operator static configurations
  Per packet information
  Per flow or per class information (i.e. state stored across packets)
  Current queue state
  Aggregated queue state (e.g. avg sizes, avg service rates)
  Other state that evolves over time
  Randomness
  Combinations of any of the above parameters
    Combined arithmetically
    Combined temporally (i.e. alternate between various policies)
    Combined hierarchically

## Slide 9: Generic Traffic Manager Architecture
Output queued
Each egress port may have many associated queues
A NIC may not need a crossbar or PRE
Classification & Policing & Drop Policy
Non-P4-Prog PRE
Non-P4-Prog Buffer
Scheduling & Shaping
Crossbar

## Slide 10: Proposed TM Architecture Model
Queue 1
Queue i
Queue N
. . .
. . .
Classification & Policing & Drop Policy
Packet Buffer
Input
Packet
Output
Packet
Scheduling / Shaping
State
Extern
interface
Ingress logic
  Classification
  Policing
  Drop Policy
Packet buffer
Scheduling / Shaping

## Slide 11: Ingress Logic
Match / Action processing
Classification:
  Decide which queue
  E.g. per flow queues
Policing:
  Is packet compliant?
  E.g. Use PSA meters to drop packets
Drop Policy:
  How to drop packets during periods of perceived congestion
  E.g. WRED
Extract scheduling metadata
Extern interface to access packet buffer state
Queue 1
Queue i
Queue N
. . .
. . .
Classification & Policing & Drop Policy
Packet Buffer
Input
Packet
Output
Packet
Scheduling / Shaping
State
Extern
interface

## Slide 12: Packet Buffer
Memory space to store packets
Divided into queues to isolate traffic
Queue boundaries may be flexible
Packet order in queue ≠ scheduling order
Exchange packet descriptor and metadata with scheduling / shaping logic
State:
  Size of each queue
  Accessible to ingress logic (read only)
Queue 1
Queue i
Queue N
. . .
. . .
Classification & Policing & Drop Policy
Packet Buffer
Input
Packet
Output
Packet
Scheduling / Shaping
State
Extern
interface
Notes: How the packets are stored in the buffer says nothing about the order in which the packets will be scheduled. It only indicates which memory slots were available when the packet arrived.

## Slide 13: The Push-In-First-Out (PIFO) Model [1]
What is a PIFO?
Why is the PIFO a good model?
  Scheduling decision made at time of enqueue  helps relax timing constraints  leads to efficient implementation
  Clear separation b/w fixed and programmable logic
Can implement existing algorithms:
  Start Time Fair Queueing (STFQ), Least Slack-Time First (LSTF), Stop-and-Go Queueing, Minimum rate guarantees, fine grained priority scheduling, Service-Curved Earliest Deadline First (SC-EDF), Rate-Controlled Service Disciplines (RCSD)
  Token bucket rate limiting
Can implement new algorithms
0
3
4
7
8
Fixed PIFO
Programmable rank computation
2

## Slide 14: Scheduling / Shaping Tree
Path computation
  Decide leaf node to enqueue into
Each node
  One PIFO
  Programmable enq and deq logic
  Potentially shared state b/w enq and deq logic
Scheduling node
  Implement scheduling algs
  Leaf nodes store descriptors, parent nodes store scheduling node refs
Shaping node
  Implement shaping algs
  Shapes all nodes within its sub tree
PIFO Scheduling / Shaping Tree
0
1
2
3
4
enq logic
deq logic
S
enq logic
0
3
deq logic
S
2
3
3
9
9
enq logic
deq logic
S
Shaping Node
Scheduling Node
t0
t1
enq logic
deq logic
S
descriptor & metadata
compute path
Queue 1
Queue i
Queue N
. . .
. . .
Classification & Policing & Drop Policy
Packet Buffer
Input
Packet
Output
Packet
Scheduling / Shaping
State
Extern
interface
Notes: Emphasize that this just an example tree

## Slide 15: Scheduling & Shaping Demonstration

## Slide 16: Scheduling and Shaping
Scheduling
Scheduling
Class A
Scheduling
Shaping
Class B
Goal:
  Enqueue 3 packets
  Dequeue 3 packets

## Slide 17: Enqueue Packet 1
p1
S
Classification / Policing /
Drop Policy
Queue 1
Queue i
Queue N
. . .
. . .
State
&p1
&p1
3
enq logic
deq logic
S
enq logic
deq logic
S
enq logic
deq logic
L
2
p1
compute path
p1
L
t1
t2
t3
t4
t5
t6
t7
t8
enq logic
deq logic
S
Shaping Node

## Slide 18: Enqueue Packet 2
p1
p2
S
Classification / Policing /
Drop Policy
Queue 1
Queue i
Queue N
. . .
. . .
State
&p2
&p1
3
enq logic
deq logic
S
enq logic
deq logic
&p2
7
L
2
p2
compute path
p2
t4
t1
t2
t3
t4
t5
t6
t7
t8
S
enq logic
deq logic
enq logic
deq logic
S
R

## Slide 19: Enqueue Packet 3
p1
p3
p2
S
Classification / Policing /
Drop Policy
Queue 1
Queue i
Queue N
. . .
. . .
State
&p3
&p1
3
enq logic
deq logic
S
enq logic
deq logic
&p3
2
&p2
7
p3
compute path
p3
t4
t7
L
2
t1
t2
t3
t4
t5
t6
t7
t8
S
enq logic
deq logic
enq logic
deq logic
S
R

## Slide 20: Enqueue Packet 2 (continued)
p1
p3
p2
S
Classification / Policing /
Drop Policy
Queue 1
Queue i
Queue N
. . .
. . .
State
&p1
3
enq logic
deq logic
S
enq logic
deq logic
&p3
2
&p2
7
compute path
t4
t7
L
2
R
R
1
t1
t2
t3
t4
t5
t6
t7
t8
S
enq logic
deq logic
enq logic
deq logic
S

## Slide 21: Dequeue Packet 3
p1
p3
p2
S
Classification / Policing /
Drop Policy
Queue 1
Queue i
Queue N
. . .
. . .
State
&p1
3
enq logic
deq logic
S
enq logic
deq logic
&p3
2
&p2
7
compute path
t7
L
2
R
1
R
&p3
t1
t2
t3
t4
t5
t6
t7
t8
S
enq logic
deq logic
enq logic
deq logic
S

## Slide 22: Dequeue Packet 1
p1
p2
S
Classification / Policing /
Drop Policy
Queue 1
Queue i
Queue N
. . .
. . .
State
&p1
3
enq logic
deq logic
S
enq logic
deq logic
&p2
7
compute path
t7
L
2
L
&p1
t1
t2
t3
t4
t5
t6
t7
t8
S
enq logic
deq logic
enq logic
deq logic
S

## Slide 23: Enqueue Packet 3 (continued)
p2
S
Classification / Policing /
Drop Policy
Queue 1
Queue i
Queue N
. . .
. . .
State
enq logic
deq logic
S
enq logic
deq logic
&p2
7
compute path
t7
R
R
1
t1
t2
t3
t4
t5
t6
t7
t8
S
enq logic
deq logic
enq logic
deq logic
S

## Slide 24: Dequeue Packet 2
p2
S
Classification / Policing /
Drop Policy
Queue 1
Queue i
Queue N
. . .
. . .
State
enq logic
deq logic
S
enq logic
deq logic
&p2
7
compute path
R
1
R
&p2
t1
t2
t3
t4
t5
t6
t7
t8
S
enq logic
deq logic
enq logic
deq logic
S

## Slide 25: Prog. Drop Policy
S
Classification / Policing /
Drop Policy
Queue 1
Queue i
Queue N
. . .
. . .
State
&p1
3
enq logic
deq logic
S
enq logic
deq logic
S
enq logic
deq logic
&p3
2
&p2
7
L
2
p4
compute path
R
1
t1
t2
t3
t4
t5
t6
t7
t8
R
1
p4
drop
Extern interface to read buffer state
Can implement WRED-like policies

## Slide 26: New Externs
/* PIFO extern */
extern pifo<T, M> {
pifo(bit<32> size); // constructor
enq(in T rank, in M meta); // meta is optional
deq(out T rank, out M meta); // meta is optional
}
// example instantiation
pifo<rank_t, sched_meta_t>(2048) p;
/* Packet buffer extern */
extern buffer<T> {
buffer(bit<32> num_queues);
// get the current size of a queue
get_q_size(in T q_id, out bit<32> size);
}
// example instantiation
buffer<qid_t>(1024) buf;

## Slide 27: Simple Architecture
parser Parser<H, M>(packet_in b,
out H hdr,
out M user_meta,
inout std_meta_t std_meta);
control Ingress<H, M, D>(inout H hdr,
out D sched_meta,
inout M user_meta,
inout std_meta_t std_meta);
scheduler MyScheduler<D>(in D sched_meta);
control Egress<H, M>(inout H hdr,
inout M user_meta,
inout std_meta_t std_meta);
control Deparser<H, M>(packet_out b,
in H hdr,
in M user_meta,
inout std_meta_t std_meta);
Ingress M/A
Ingress Parser
Egress Deparser
Egress M/A
Scheduling / Shaping
Non-P4-Programmable PRE / buffer
Classification & Policing & Drop Policy
User defined scheduling metadata

## Slide 28: Scheduler Block
scheduler MyScheduler(in sched_meta_t sched_meta)
{
/* Define PIFO tree nodes */
/* root node */
node strict_priority {
type = scheduling;
pifo<rank_t>(2048) p;
enqueue = { }
dequeue = { }
} /* shaping node */
node token_bucket {
type = shaping;
pifo<rank_t, sched_meta_t>(2048) p; enqueue = { } dequeue = { }
} /* Define the shape of the tree */
tree myTree { strict_priority(), {wfq(), {token_bucket(), {wfq()} } } table find_path { } apply {
find_path.apply();
// apply the scheduling algorithm defined by the tree
myTree.apply(leaf_node);
}
}
strict
WFQ
WFQ
token bucket

## Slide 29: Example – Strict Priority
/* root node */
node strict {
type = scheduling;
// PIFO extern instantiation format:
// pifo<rank_type>(size_in_pkts) instance_name;
pifo<rank_t>(2048) p;
enqueue = {
rank_t rank;
rank = sched_meta.diffserv; // maybe use a table?
p.enq(rank);
}
dequeue = {
rank_t rank;
p.deq(rank);
}
}
Strict
Class A
Class B
high
low

## Slide 30: Example – Strict Priority with Starvation Prevention
FCFS nodes prevent reordering of packets within a flow
Also useful for traffic that is sensitive to jitter (e.g. voice)
strict
FCFS
FCFS
token bucket
high
low
Flow A
Flow B

## Slide 31: Example – Strict Priority with Starvation Prevention
node token_bucket {
type = shaping;
pifo<rank_t, sched_meta_t>(2048) p;
enqueue = {
// declare registers: tb, last_time, rate, max_tokens
@atomic {
// atomically update last_time and tb registers
tb.read(0, old_tokens);
old_tokens = old_tokens + r * (now - lt);
if (old_tokens > B) {
old_tokens = B;
}
// compute new tokens and send time
if (sm.pkt_len <= old_tokens) {
new_tokens = old_tokens – sm.pkt_len;
send_time = now;
} else {
new_tokens = 0;
send_time = now + (sm.pkt_len – old_tokens)/r;
}
tb.write(0, new_tokens);
}
p.enq(send_time, sm);
}
dequeue = {
bit<rank_t> rank;
p.deq(rank, sm);
}
}
strict
FCFS
FCFS
token bucket
high
low
Flow A
Flow B

## Slide 32: Example – Strict Priority with Starvation Prevention
node FCFS {
type = scheduling;
pifo<rank_t>(2048) p;
enqueue = {
bit<rank_t> rank = get_time(); // extern function
p.enq(rank);
} dequeue = {
bit<rank_t> rank;
p.deq(rank);
}
}
/* Define the shape of the tree */
tree myTree { strict_priority(), {FCFS(), {token_bucket(), {FCFS()}}} } apply {
// path computation logic
pifo_id_t leaf_node;
if (sched_meta.flow_id == 0) {
leaf_node = RIGHT;
} else {
leaf_node = LEFT;
}
// apply the scheduling / shaping algorithm
myTree.apply(leaf_node);
}
strict
FCFS
FCFS
token bucket
high
low
Flow A
Flow B

## Slide 33: Example – Low Latency Traffic
WFQ across all queues until a particular queue exceeds a configured threshold at which point that queue is given strict priority until it has been sufficiently drained
Classification sets desired queue size in sched_meta
low latency
FCFS
Flow A
FCFS
Flow B
FCFS
Flow C

## Slide 34: Example – Low Latency Traffic
Ingress Logic:
buffer<qid_t>(NUM_QUEUES) buf; // instantiate buffer extern
// get size of low latency queue
sched_meta.ll_q_size = buf.get_q_size(LL_Q_ID);
lookup_queue.apply(); // set egress queue
Root Node:
node low_latency {
type = scheduling;
pifo<rank_t>(2048) p;
enqueue = {
if (sched_meta.ll_q_size > THRESH) {
// Strict priority logic
} else {
// WFQ logic
}
p.enq(rank);
}
dequeue = {
rank_t rank;
p.deq(rank);
}
}
low latency
FCFS
Flow A
FCFS
Flow B
FCFS
Flow C

## Slide 35: Runtime Control
The tree can be updated by the control plane, but not from within the P4 program
  Akin to adding table entries
Will need P4Runtime support for tree configuration
Tables and externs can be handled normally

## Slide 36: Open Source Implementations
NetFPGA Prototype (P4 Workshop Demo)
Packet Buffer
Input
Packet
rank computation
Queue 1
Queue i
Queue N
. . .
. . .
0
3
4
7
8
Classification
descriptor & metadata
descriptor & rank
descriptor
PIFO Scheduler
Output
Packet
2
3
5
5
4
2
4
6
8
A
B
C
Rank Store
(SRAM)
Flow Scheduler
(flip-flops)
C 3
B 1
A 0
Increasing ranks
Increasing ranks
PIFO block diagram
PIFO paper ASIC design [1]
Notes: # pkts, resource consumption, max rate, # queues

## Slide 37: Challenges with TM Programmability
Scaling programmable designs to high rates and large sizes
  Bottleneck #1 – timing closure for scheduling decision logic
  Bottleneck #2 – memory bandwidth/interface to large packet buffer
Abstractions to program the PIFO tree
Limitations of the proposed model

## Slide 38: Moving Forward
Motivation from the community?
Settle on architecture model
Define language semantics
  Is a tree too low-level?
  Are there better abstractions?
Improve open source HW implementations
Open source simulation/emulation environment
  Bmv2? NS3? Other?
Small P4 TM Working Group
Notes: Moving forward with P4.org:
Small working group of people that are interested, maybe bi-weekly meetings
  Settle on TM architectural model
  Draft P4 lang extensions on top of model
  Present to P4 Lang working group
Settle on language extensions
Eventually gets to API WG as well

## Slide 39: References
[1] Anirudh Sivaraman, Suvinay Subramanian, Mohammad Alizadeh, Sharad Chole, Shang-Tse Chuang, Anurag Agrawal, Hari Balakrishnan, Tom Edsall, Sachin Katti, Nick McKeown. "Programmable packet scheduling at line rate." Proceedings of the 2016 ACM SIGCOMM Conference https://cs.nyu.edu/~anirudh/pifo-sigcomm.pdf

## Slide 40: Questions?

## Slide 41: NetFPGA Prototype (P4 Workshop Demo)
Parallel deterministic skip lists and register-based sorting cache
BRAM based packet buffer
Packet Buffer
Input
Packet
rank computation
Queue 1
Queue i
Queue N
. . .
. . .
0
3
4
7
8
Classification
descriptor & metadata
descriptor & rank
descriptor
PIFO Scheduler
Output
Packet
Load Balancer
Selector
Register Cache
Skip List
Register Cache
Skip List
Register Cache
Skip List
Register Cache
. . .
Insertion
Removal
Top level PIFO block diagram
Notes: # pkts = 2048
buffer size = 130KB
Max rate = 10Gbps for 64B pkts
# queues = 4
Resource consumption = 10-15% of V7

## Slide 42: PIFO Paper ASIC Design [1]
Flow scheduler
  Choose amongst head pkt of each flow
Rank Store
  Store computed ranks for each flow in FIFO order
PIFO blocks connected in a full mesh
64 port 10Gbps shared memory switch, 1GHz
1000 flows, 64K packets
2
3
5
5
4
2
4
6
8
A
B
C
Rank Store
(SRAM)
Flow Scheduler
(flip-flops)
C 3
B 1
A 0
Increasing ranks
Increasing ranks
PIFO block diagram

## Slide 43: TM Model Limitations

## Slide 44: Input vs Output Rate Limiting
Goal of rate limiting: control the rate at which bytes are removed from the buffer and scheduled.
  Output rate limiting – direct approach, short and long term rate guarantees
  Input rate limiting – indirect approach, long term rate guarantees
Strict
FCFS
low
high
FCFS
Sent out at line rate
Rate Limit

## Slide 45: Arbitrary reordering of buffered packets
6
p3
Pfabric scheduling order:
  SRPT with FIFO order within flows
8
p2
9
p1
7
p0

## Slide 46: Approximate Pfabric
SRPT
FCFS
FCFS
7
p0
0
p0
7
p0
7
L
9
p1
9
p1
0
p1
9
R
8
p2
8
p2
1
p2
8
R
6
p3
6
p3
2
p3
6
R
p1
p0
p2
p3
Final Scheduling Order:
p1
p0
p2
p3
Pfabric Scheduling Order:

## Slide 47: Soft Rate Limiting
“Rate limit flow A to 2 Gbps only if the egress link is congested”
Hard vs. Soft Rate Limiting:
  Hard – hold packets until time to send (non work conserving)
  Soft – packets can be sent if bandwidth is available (work conserving)

## Slide 48: Soft Rate Limiting
p2
S
Classification / Policing /
Drop Policy
Queue 1
Queue i
Queue N
. . .
. . .
State
enq logic
deq logic
S
enq logic
deq logic
&p2
7
compute path
t7
t1
t2
t3
t4
t5
t6
t7
t8
&p2
default
S
enq logic
deq logic
enq logic
deq logic
S
What if there are multiple shaping nodes?
R

## Slide 49: Ingress Logic Limitations
Drop policy:
  No drop head algorithms (unless using speedup)
No algorithms that must programmatically update state in the packet buffer

## Slide 50: Best Effort for Traffic Shaping
Shaping operations cause conflicts
  Scheduling and shaping transactions commit at same time
  Resolved in favor of scheduling transactions
  Rationale: scheduling algorithms must run at line rate, shaping algorithms can afford to be delayed a few cycles

## Slide 51: Enqueue Conflict
p4
p1
p3
p2
S
Classification / Policing /
Drop Policy
Queue 1
Queue i
Queue N
. . .
. . .
State
&p1
3
enq logic
deq logic
S
enq logic
deq logic
&p3
2
&p2
7
compute path
t4
t7
L
2
R
t1
t2
t3
t4
t5
t6
t7
t8
&p4
p4
p4
L
&p4
5
L
2
S
enq logic
deq logic
enq logic
deq logic
S

## Slide 52: Constraints
1 enqueue and 1 dequeue at each level of tree per time slot
Need to deal with wrap around of rank values

## Slide 53: Scheduling Demonstration

## Slide 54: Scheduling
Scheduling
Scheduling
Class A
Scheduling
Class B
Goal:
  Enqueue 3 packets
  Dequeue 3 packets

## Slide 55: Enqueue Packet 1
p1
S
Classification / Policing /
Drop Policy
Queue 1
Queue i
Queue N
. . .
. . .
State
&p1
&p1
3
enq logic
deq logic
S
enq logic
deq logic
S
enq logic
deq logic
L
2
p1
compute path
p1
L
t1
t2
t3
t4
t5
t6
t7
t8

## Slide 56: Enqueue Packet 2
p1
p2
S
Classification / Policing /
Drop Policy
Queue 1
Queue i
Queue N
. . .
. . .
State
&p2
&p1
3
enq logic
deq logic
S
enq logic
deq logic
S
enq logic
deq logic
&p2
7
L
2
R
1
p2
compute path
p2
R
t1
t2
t3
t4
t5
t6
t7
t8

## Slide 57: Enqueue Packet 3
p1
p3
p2
S
Classification / Policing /
Drop Policy
Queue 1
Queue i
Queue N
. . .
. . .
State
&p3
&p1
3
enq logic
deq logic
S
enq logic
deq logic
S
enq logic
deq logic
&p3
2
&p2
7
L
2
R
1
p3
compute path
p3
R
R
1
t1
t2
t3
t4
t5
t6
t7
t8

## Slide 58: Dequeue Packet 3
p1
p3
p2
S
Classification / Policing /
Drop Policy
Queue 1
Queue i
Queue N
. . .
. . .
State
&p1
3
enq logic
deq logic
S
enq logic
deq logic
S
enq logic
deq logic
&p3
2
&p2
7
L
2
R
1
compute path
R
1
R
&p3
t1
t2
t3
t4
t5
t6
t7
t8

## Slide 59: Dequeue Packet 2
p1
p2
S
Classification / Policing /
Drop Policy
Queue 1
Queue i
Queue N
. . .
. . .
State
&p1
3
enq logic
deq logic
S
enq logic
deq logic
S
enq logic
deq logic
&p2
7
L
2
compute path
R
1
R
&p2
t1
t2
t3
t4
t5
t6
t7
t8

## Slide 60: Dequeue Packet 1
p1
S
Classification / Policing /
Drop Policy
Queue 1
Queue i
Queue N
. . .
. . .
State
&p1
3
enq logic
deq logic
S
enq logic
deq logic
S
enq logic
deq logic
L
2
compute path
L
&p1
t1
t2
t3
t4
t5
t6
t7
t8

## Slide 61: Additional Examples

## Slide 62: Example – Shortest Remaining Processing Time (SRPT)
Ingress Logic:
table lookup_queue {
key = { sched_meta.rank: ternary; }
actions = { set_queue; }
size = 1024;
default_action = set_default_queue;
}
// apply block
sched_meta.rank = hdr.bytes_remaining;
lookup_queue.apply();
Scheduling Node:
node SRPT {
type = scheduling;
pifo<rank_t>(2048) p;
enqueue = { p.enq(sched_meta.rank); }
dequeue = {
rank_t rank;
p.deq(rank);
}
}
SRPT
Flow A
Flow X
. . .
Notes: Implemented in NetFPGA prototype

## Slide 63: Example – Weighted Fair Queueing (WFQ)
node wfq {
// PIFO extern instantiations
pifo<rank_t>(2048) p;
// virtual_time state to track last rank dequeued
register<rank_t>(1) virtual_time; enqueue = {
// declare weight & last_finish reg arrays
// read virtual_time
virtual_time.read(0, vt);
@atomic {
last_finish.read(flow_id, lf);
if (lf != 0) {
// seen this flow before
start = max(vt, lf);
} else {
start = vt;
}
weight.read(flow_id, fw)
lf = start + sched_meta.pkt_len/fw;
last_finish.write(flow_id, lf);
}
rank = start;
p.enq(rank);
}
dequeue = {
bit<16> rank;
p.deq(rank);
virtual_time.write(0, rank);
}
}
WFQ
Class A
Class C
Class B

## Slide 64: Example – Strict Priority w/ WFQ
/* Define the shape of the tree */
tree myTree { strict(), {WFQ(), WFQ()} }
table find_path { } apply {
// path computation logic
find_path.apply();
// apply the scheduling / shaping algorithm
myTree.apply(leaf_node);
}
WFQ
Class C
Class D
WFQ
Class A
Class B
Strict
high
low

## Slide 65: Example – Bandwidth Reservations (Min Rate Guarantees)
Root computes rank as either 0 (below min rate) or 1 (above min rate)
FCFS used to prevent reordering within a flow
Strict (Min Rate)
FCFS
Flow A
FCFS
Flow B
FCFS
Flow C

## Slide 66: More Examples
Heavy hitter detection to map HH flows to separate queue and assign their packets lower priority
Scheduling transaction computes level of burstiness for each flow and assigns priority as the inverse of the burstiness – encourages smooth traffic