## Slide 1: A P4 v1.2 example
Mihai Budiu
Barefoot Networks
February 2016

## Slide 2: P4 v1.2
P4 v1.0 / v1.1
P4 v1.2 core
stdlib.p4
arch_library.p4
arch.p4
small,
rarely change
unbounded,
frequent changes

## Slide 3: The parts
P4 v1.2 core
stdlib.p4
arch_library.p4
arch.p4
Language syntax and semantics (parsers, controls, actions, tables, etc.)
Built-in constructs (packet, error codes, etc.)
Extern definitions
Prototypes (parser, control, package)

## Slide 4: Scope of presentation
P4 v1.2 core
stdlib.p4
arch_library.p4
arch.p4
See previous design group presentation: “towards p4 v1.2”
See previous presentation:
“abstracting switches”
“Simple” example
we don’t cover all language aspects today

## Slide 5: P4 Program structure
// simple-switch-example.p4
#include “stdlib.p4”
#include “simple.p4”
// User-code
header Ethernet_h { … }
…

## Slide 6: stdlib.p4 – Part 1
#ifndef _STDLIB_P4_ #define _STDLIB_P4_
struct Version { bit<8> major; bit<8> minor; }
const Version P4_LIBRARY_VERSION = { 8w0, 8w1 };
error { NoError, // no error PacketTooShort, // not enough bits in packet for extract NoMatch, // match expression has no matches EmptyStack, // reference to .last in an empty header stack FullStack, // reference to .next in a full header stack OverwritingHeader // one header is extracted twice }
…
#endif

## Slide 7: stdlib.p4 – Part 2: the packet interfaces
extern packet_in { void extract<T>(out T hdr); // T must be a varbit type. void extract<T>(out T varSzHdr, in bit<32> szInBits); // does not advance the cursor T lookahead<T>(); }
extern packet_out { void emit<T>(in T hdr); }
packet_in

## Slide 8: stdlib.p4 – Part 3
extern void assert(in bool check, in error toSignal);
action NoAction() {}
match_kind { exact, ternary, lpm, range }
No longer built-in;
extensible

## Slide 9
Match-action pipeline
Deparser
Input headers
Output headers
inControl
outControl
Demux/ queue
To CPU
Arbiter
Packets in
Packets out
Drop
From CPU
error
Recirculate
Packet
Parser
The “Simple” switch architecture modeled
P4 programmable-blocks

## Slide 10: simple.p4 – part 1: components library
#ifndef _SIMPLE_P4_ #define _SIMPLE_P4_ // Architecture definition file for the "Simple" switch
#include "stdlib.p4”
extern Checksum16 { // prepare unit void clear(); // add data to be checksummed void update<D>(in D dt); // conditionally add data to be checksummed void update<D>(in bool condition, in D dt); // get the checksum of all data added since the last clear bit<16> get();
}
…
#endif
Checksum unit is a library
component.

## Slide 11: simple.p4 – Part 2: metadata definitions
/* ports are represented using 4-bit values */ typedef bit<4> PortId_t;
/* only 8 ports are “real” */ const PortId_t REAL_PORT_COUNT = (PortId_t)4w8;
/* metadata accompanying an input packet */ struct InControl { PortId_t inputPort; }
/* special input port values */ const PortId_t RECIRCULATE_INPUT_PORT = (PortId_t)4w0xD; const PortId_t CPU_INPUT_PORT = (PortId_t)4w0xE;
/* metadata that must be computed for outgoing packets */ struct OutControl { PortId_t outputPort; }
/* special output port values for outgoing packet */ const PortId_t DROP_PORT = (PortId_t)4w0xF; const PortId_t CPU_OUT_PORT = (PortId_t)4w0xE; const PortId_t RECIRCULATE_OUT_PORT = (PortId_t)4w0xD;

## Slide 12: simple.p4 – Part 3: switch architecture
/* List of blocks that must be implemented */ parser Parser<H>(packet_in b, out H parsedHeaders);
control MAP<H>(inout H headers, in error parseError, // parser error in InControl inCtrl, // input port out OutControl outCtrl); // output port
control Deparser<H>(inout H outputHeaders, packet_out b);
/* H is the user-defined type of the headers */ package Simple<H>(Parser<H> p, MAP<H> map, Deparser<H> d);

## Slide 13: The user program – Part 1
#include "stdlib.p4”
#include "simple.p4”
// This program processes packets composed of an Ethernet and // an IPv4 header, performing forwarding based on the // destination IP address
typedef bit<48> @ethernetaddress EthernetAddress; typedef bit<32> @ipv4address IPv4Address;

## Slide 14: User program – Part 2: header declarations
header Ethernet_h { EthernetAddress dstAddr; EthernetAddress srcAddr; bit<16> etherType; }
// IPv4 header without options header IPv4_h { bit<4> version; bit<4> ihl; bit<8> diffserv; bit<16> totalLen; bit<16> identification; bit<3> flags; bit<13> fragOffset; bit<8> ttl; bit<8> protocol; bit<16> hdrChecksum; IPv4Address srcAddr; IPv4Address dstAddr; }

## Slide 15: User program – Part 3: interface to Parser
error { IPv4IncorrectVersion, IPv4OptionsNotSupported, IPv4ChecksumError }
struct Parsed_packet { Ethernet_h ethernet; IPv4_h ip; }
User-defined error codes.

## Slide 16: User program – part 4: Packet parser
parser TopParser(packet_in b, out Parsed_packet p) { Checksum16() ck;
state start { b.extract(p.ethernet); transition select(p.ethernet.etherType) { 16w0x0800 : parse_ipv4; } }
state parse_ipv4 { b.extract(p.ip); assert(p.ip.version == 4w4, IPv4IncorrectVersion); assert(p.ip.ihl == 4w5, IPv4OptionsNotSupported); ck.clear(); ck.update(p.ip); assert(ck.get() == 16w0, IPv4ChecksumError); transition accept; } }

## Slide 17: User program – Part 5: Deparser
control TopDeparser(inout Parsed_packet p, packet_out b) { Checksum16() ck; apply {
b.emit(p.ethernet); if (p.ip.valid) { ck.clear(); // prepare checksum unit p.ip.hdrChecksum = 16w0; // clear checksum ck.update(p.ip); // compute new checksum p.ip.hdrChecksum = ck.get(); } b.emit(p.ip); } }

## Slide 18: User program – Part 6: Pipeline structure
control Pipe(inout Parsed_packet headers, in error parseError, // parser error in InControl inCtrl, // input port out OutControl outCtrl) {
action Drop_action(...) { ... } action Set_nhop(...) { ... }
table ipv4_match { ... }
action Send_to_cpu(...) { ... }
table check_ttl() { ... }
action Set_dmac(...) { ... }
table dmac(...) { ... }
action Rewrite_smac(...) { ... }
table smac() { ... }
apply { ... } }

## Slide 19: User Program – Part 7: Action declaration
/** * Indicates that a packet is dropped by setting the * output port to the DROP_PORT * @param port output port to set */ action Drop_action(out PortId_t port) { port = DROP_PORT; }

## Slide 20: User Program – Part 8: Complex action
/** * Set the next hop and the output port * @param ivp4_dest ipv4 address of next hop * @param port output port */ action Set_nhop(out IPv4Address nextHop, IPv4Address ipv4_dest, PortId_t port) { nextHop = ipv4_dest; headers.ip.ttl = headers.ip.ttl – 8w1; outCtrl.outputPort = port; }
From enclosing control block.
Parameters bound by the control plane
Bound by compiler.

## Slide 21: User Program – Part 9: table
/** * Computes address of next IPv4 hop and output port * based on the IPv4 destination of the current packet. * Decrements packet IPv4 TTL. * @param nextHop IPv4 address of next hop */ table ipv4_match(out IPv4Address nextHop) {
key = { headers.ip.dstAddr : lpm; }
actions = { Set_nhop(nextHop); Drop_action(outCtrl.outputPort); }
size = 1024;
default_action = Drop_action(outCtrl.outputPort); }

## Slide 22: User Program - Part 10: Control body
apply { if (parseError != NoError) { Drop_action(outCtrl.outputPort); return; }
IPv4Address nextHop; // temporary variable ipv4_match.apply(nextHop); if (outCtrl.outputPort == DROP_PORT) return; check_ttl.apply(); if (outCtrl.outputPort == CPU_OUT_PORT) return; dmac.apply(nextHop); if (outCtrl.outputPort == DROP_PORT) return; smac.apply(); }

## Slide 23: User Program – Part 11: Switch instantiation
Simple( TopParser(), Pipe(), TopDeparser() ) main;
Constructors.